## Slide 1
Buffer overflow
Mihir Shah
20th Apr 2019

## Slide 2
About Today
x32 Arch Basic
- Basics of Buffer Overflow
- Basics of Immunity Debugger
- Vanilla Buffer Overflow

## Slide 3
x32 Arch basic(assembly basic)

## Slide 4
System Organization Basics

## Slide 5
CPU
Execution Unit
Control Unit
Registers
Flags
Control Unit : Retrieve/Decode instructions, Retrieve/Store data in memory
Execution Unit : Actual execution of instruction happens here
Registers : Internal memory locations used as “variables”
Flags : Used to indicate various “event” when execution is happening

## Slide 6
CPU REGISTERS
EAX |  | EBX |  | ECX |  | EDX |  | ESI |  | EDI |  | ESP |  | EBP
General Purpose Registers
CS |  | DS |  | SS |  | ES |  | FS |  | GS
Segment Registers
EIP
Instruction Pointer Register
CR0 |  | CR1 |  | CR2 |  | CR3 |  | CR4
Control Registers

## Slide 7
EAX |  |  |  | Accumulator Register – used for storing operands and result data
EBX |  |  |  | Base Register – Pointer to data
ECX |  |  |  | Counter Register – Loop Operations
EDX |  |  |  | Data Register – I/O Pointer
ESI |  | EDI |  | Data Pointer Registers for memory operations
ESP |  |  |  | Stack Pointer Register
EBP |  |  |  | Stack Data Pointer Register
Notes: 7

## Slide 8
EAX |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  | 0 | 
 |  |  | AX |  |  |  |  | 
31 | 16 |  | 15 |  |  | 0 |  | 
 |  |  | AH |  |  | AL |  | 
 |  |  | 15 | 8 |  | 7 |  | 0
EAX
Notes: <number>

## Slide 9
EBX |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  | 0 | 
 |  |  | BX |  |  |  |  | 
31 | 16 |  | 15 |  |  | 0 |  | 
 |  |  | BH |  |  | BL |  | 
 |  |  | 15 | 8 |  | 7 |  | 0
EBX

## Slide 10
ECX |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  | 0 | 
 |  |  | CX |  |  |  |  | 
31 | 16 |  | 15 |  |  | 0 |  | 
 |  |  | CH |  |  | CL |  | 
 |  |  | 15 | 8 |  | 7 |  | 0
ECX

## Slide 11
EDX |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  | 0 | 
 |  |  | DX |  |  |  |  | 
31 | 16 |  | 15 |  |  | 0 |  | 
 |  |  | DH |  |  | DL |  | 
 |  |  | 15 | 8 |  | 7 |  | 0
EDX

## Slide 12
Four 32-bit data registers are used for arithmetic, logical, and other operations.
These 32-bit registers can be used in three ways −
As complete 32-bit data registers: EAX, EBX, ECX, EDX
Lower halves of the 32-bit registers can be used as four 16-bit data registers: AX, BX, CX and DX
Lower and higher halves of the above-mentioned four 16-bit registers can be used as eight 8-bit data registers: AH, AL, BH, BL, CH, CL, DH, and DL
Some of these data registers have specific use in arithmetical operations.
AX is the primary accumulator; it is used in input/output and most arithmetic instructions. For example, in multiplication operation, one operand is stored in EAX or AX or AL register according to the size of the operand.
BX is known as the base register, as it could be used in indexed addressing.
CX is known as the count register, as the ECX, CX registers store the loop count in iterative operations.
DX is known as the data register. It is also used in input/output operations. It is also used with AX register along with DX for multiply and divide operations involving large values.

## Slide 13
Basic of Buffer Overflow

## Slide 14
Buffer
Small memory allocated for a specific input
System memory
Buffer

## Slide 15
void main()
{
char source[ ] = “HELLO”; // HELLO assigned to source
char destination[2]; // destination is 3 bytes
strcpy(destination, source); // copy source to destination
return 0;
}
Buffer (3 bytes) |  |  | Overflow | 
H | E | L | L | O
0 | 1 | 2 | 3 | 4

## Slide 16
STACK

## Slide 17
ESP (Extended Stack Pointer (top))
Buffer Space
EBP (Extended Base Pointer (base))
Return Address
Parent Routine’s Stack
Stack Growth
Memory Addresses

## Slide 18
Stack is LIFO (Last In First Out)
0xAAAAAAAA
0x10203040
High Memory
Low Memory
ESP
ESP – Should point to top of Stack

## Slide 19
Stack is LIFO (Last In First Out)
0xAAAAAAAA
0x10203040
0xA0203040
High Memory
Low Memory
ESP
ESP – Should point to top of Stack
Push – Pushes a value onto the Stack

## Slide 20
Stack is LIFO (Last In First Out)
0xAAAAAAAA
0x10203040
High Memory
Low Memory
ESP
ESP – Should point to top of Stack
Push – Pushes a value onto the Stack
Pop – Removes the topmost value from the Stack